## Slide 1
SPEECH ENHANCEMENT AND NOISE REMOVAL
Simple DSP approach for making noisy speech clearer
R. Sai Samartha Reddy • Sriram Kanuri • Rishi Vardhan Guide: Dr. V Sahiti | ECE | KL University, Hyderabad

## Slide 2
1. Introduction
Why do we need speech enhancement?
The Problem
Real-world speech often contains background noise. Examples: fan, traffic, people, machines.
Our Idea
Take noisy speech → analyze its frequencies → reduce unwanted components → get cleaner speech.
Goal
Improve speech quality while keeping the important speech information.
2

## Slide 3
2. Problem Statement
Noise hides the speech we want to hear
• Background noise reduces speech clarity.
• Important speech components can be affected.
• Overall signal quality becomes lower.
• Noisy speech can reduce the reliability of speech-based applications.
• We need to reduce noise without losing important speech information.
3

## Slide 4
3. Objectives
What do we want our system to do?
Main Objective
Remove unwanted noise while preserving useful speech.
FFT
Analyze the signal in the frequency domain.
Filter
Attenuate unwanted frequency components.
Compare
Check original, noisy and enhanced speech.
SNR
Measure whether the signal quality improved.
4

## Slide 5
4. Literature Survey
What previous researchers have done
Boll (1979)
Spectral subtraction. Frequency-domain noise suppression. Can leave residual artifacts.
Ephraim & Malah (1984)
MMSE-STSA. Statistical speech enhancement with higher computational complexity.
Ephraim & Malah (1985)
MMSE-LSA. Log-spectral statistical enhancement.
Scalart & Vieira Filho (1996)
A-priori SNR based enhancement. Depends on noise estimation.
Our Gap / Approach
Start with a simple, transparent and reproducible DSP baseline, then extend it toward ML.
5

## Slide 6
5. Existing System vs Proposed System
What is different about our approach?
Existing / Conventional
• Limited frequency analysis • Limited quantitative evaluation • Less reproducible workflow • No integrated analysis + visualization + measurement
Proposed System
• Python-based SP • Controlled noise testing • FFT analysis • 6th-order Butterworth LPF • Waveform + spectrum comparison • SNR evaluation • Reproducible workflow
6

## Slide 7
6. Proposed Methodology
The complete process
1. Speech WAV
Input speech
2. Pre-process
Mono + normalize
3. Add noise
Gaussian white noise
4. FFT
See frequency components
5. Filter
6th-order Butterworth LPF Cutoff = 4 kHz
6. Evaluate
Waveform + spectrum + SNR
7

## Slide 8
7. What are FFT and SNR used for?
Two different jobs
FFT = Analysis 🔍
FFT changes the signal from time domain to frequency domain. It helps us see which frequencies are present and observe the effect of filtering.
SNR = Measurement 📊
SNR tells us how strong the useful signal is compared with noise. Higher SNR generally means better signal quality. Our Phase 1 result: 8.18 dB → 14.86 dB.
8

## Slide 9
8. System Requirements
Software-only project
Software
Python 3 NumPy SciPy Matplotlib Windows / Linux WAV audio input
Hardware
Modern x86-64 processor Minimum 4 GB RAM About 1 GB+ storage No dedicated DSP hardware
Implementation
100% software Can run from a terminal or Python environment. Easy to reproduce.
9

## Slide 10
9. Phase 1 Results
Did the filtering improve the signal?
BEFORE
SNR 8.18 dB
AFTER
SNR 14.86 dB
IMPROVEMENT
+6.69 dB
Experiment
Speech WAV + Gaussian white noise + 6th-order Butterworth LPF + 4 kHz cutoff
10

## Slide 11
10. Future Scope
DSP baseline → more advanced system
Phase 2: Better SP
• Real-world noise types • Compare digital filters • Try different cutoff frequencies • Use larger speech datasets
Phase 3: Machine Learning
• Extract spectral features • Train noise-estimation models • Explore CNNs / autoencoders • Compare DSP vs ML
Evaluation
SNR PESQ STOI MSE Spectral analysis
11

## Slide 12
11. References
Key research used in the project
• Boll, S. F. (1979), IEEE TASSP – Spectral Subtraction.
• Ephraim & Malah (1984), IEEE TASSP – MMSE-STSA.
• Ephraim & Malah (1985), IEEE TASSP – MMSE-LSA.
• Scalart & Vieira Filho (1996), ICASSP – A-priori SNR based enhancement.
12